## Slide 1: Physics-inspired Neural Networks for building modeling and control
Loris Di Natale 1,2 Bratislav Svetozarevic 1 Philipp Heer 1 Colin N. Jones 2
1Urban Energy Systems Lab, Empa, Switzerland
2Automatic Control Lab, EPFL, Switzerland
American Control Conference 2023, San Diego

## Slide 2: Neural Networks and physical systems
Neural Networks (NNs) achieve amazing performance…
… but can also fail spectacularly
  They only do exactly what they are taught
What about controlling (real-world) physical systems with NNs?
  Data quantity/quality issues
  Time to converge
  Exploration phase
  Guarantees?
******
Go back to simulation
The Guardian
NEST, Empa, Dübendorf
Switzerland, © Zooey Braun
Notes: Just some of many many examples
Building as running examples in this talk
Data for pretraining

## Slide 3: Neural Networks and physical systems
Trained sequentially from data
Can choose to use a NN to model the system as well
Controller
Model
Data
train
train
deploy
It works! Can save 25-30% of energy on UMAR compared to industrial baselines,[1] but…
Notes: On this specific building

## Slide 4: Neural Networks are physics-agnostic
They attain great accuracy
They can violate physical laws [2,3]
Model
Heating and cooling have almost no (or even reversed) impact
Can we help NNs?
We often have some prior knowledge of the system
Notes: In the case of physical systems
We (often) know a lot about the system to control
  Simplified model
  Simplified controller
  …
 Prior (physical) knowledge of the system

## Slide 5: PiNNs for supervised learning
Given a dataset
Model
backpropagation
Notes: Learning from scratch is the usual way

## Slide 6: PiNNs for supervised learning
Given a dataset
Main idea: Modified loss function to steer the NN towards expected solutions
  Boundary conditions
  Physical laws (energy/mass/momentum conservation, …)
backpropagation
Model
Notes: Learning from scratch is the usual way
Here say physics but can be any type of knowledge really

## Slide 7: Do PiNNs work?
Want to ensure physical consistency: [3]
Idea: heating must heat the building
Model
Does not solve our issues!
Notes: In the case of physical systems
Again, there are a lot of ways to go about it, we chose this formulation

## Slide 8: PiNNs for supervised learning
Model
Pros
Ease of implementation
Can accelerate learning
Can improve the solution
Cons
Hyperparameter tuning
No guarantees
Whenever possible, you can also try to use tailored architectures
Modified physical losses are a good start to help NNs
Hamiltonian NNs,[4] Lagrangian NNs,[5] …
Notes: In the case of physical systems

## Slide 9: Physically Consistent NNs (PCNNs) [6]
Let a basic physics-inspired module run in parallel of the NN
Key: Train simultaneously through backpropagation
State-of-the-art accuracy on the analyzed case study
But following the laws of physics
Model

## Slide 10: Neural Networks and physical systems
Controller
Model
Data
train
train
deploy
If you have a good model, you can use MPC, unless it is impractical

## Slide 11: PiNNs for reinforcement learning
Learning through interaction with the environment
Controller
Environment
Notes: Might be interesting if you know the output is some combination of three variables e.g. – encourages the NN to find these variables and then predict the output from them

## Slide 12: PiNNs for reinforcement learning
Learning through interaction with the environment
Reward shaping: modify the feedback to the network (e.g., constraints violations, …)
Controller
Environment
Notes: Sort of the equivalent to PiNNs in supervised learning – could also add an output or a bottleneck to the network and penalize it in the reward if there is something else we want

## Slide 13: PiNNs for reinforcement learning
Learning through interaction with the environment
Reward shaping: modify the feedback to the network (e.g., constraints violations, …)
Residual learning: additive, multiplicative, time varying, …
Controller
Environment
Notes: Might be interesting if you know the output is some combination of three variables e.g. – encourages the NN to find these variables and then predict the output from them

## Slide 14: PiNNs for reinforcement learning
Learning through interaction with the environment
Reward shaping: modify the feedback to the network (e.g., constraints violations, …)
Residual learning: additive, multiplicative, time varying, …
Shielding: Define a filter to correct the agent when some specifications are not met
Controller
Environment
Shield
Notes: Might be interesting if you know the output is some combination of three variables e.g. – encourages the NN to find these variables and then predict the output from them

## Slide 15: PiNNs for reinforcement learning
Learning through interaction with the environment
Reward shaping: modify the feedback to the network (e.g., constraints violations, …)
Residual learning: additive, multiplicative, time varying, …
Shielding: Define a filter to correct the agent when some specifications are not met
  Project on the desired set
Controller
Environment
Shield
Notes: Might be interesting if you know the output is some combination of three variables e.g. – encourages the NN to find these variables and then predict the output from them

## Slide 16: PiNNs for reinforcement learning
Learning through interaction with the environment
Reward shaping: modify the feedback to the network (e.g., constraints violations, …)
Residual learning: additive, multiplicative, time varying, …
Shielding: Define a filter to correct the agent when some specifications are not met
  Project on the desired set
  Use a known fallback controller
Controller
Environment
Shield
Notes: Might be interesting if you know the output is some combination of three variables e.g. – encourages the NN to find these variables and then predict the output from them

## Slide 17: PiNNs for reinforcement learning
Introducing physics/knowledge can accelerate learning and lead to better solutions
Controller
Pros
Ease of implementation
Computationally cheap
Can get guarantees
Preserves knowledge
Cons
No guarantees
Can dilute knowledge
Comp. expensive
Design of ?
Reward shaping
Residual learning
Shielding
Can we improve the computational efficiency of shielding to enforce prior knowledge?
Notes: Might be interesting if you know the output is some combination of three variables e.g. – encourages the NN to find these variables and then predict the output from them

## Slide 18: Computationally Efficient RL [7]
Use time-varying bounds on the agent’s actions to avoid suboptimal state-action pairs
The projection is computationally cheap: saturate the actions at each step!
Modify the gradient update of the agent so it learns from its mistakes
Controller
“If it’s too cold, then heat”
”If it’s too hot, then don’t heat”
…
No computational overhead
but no guarantees

## Slide 19: Computationally Efficient RL [7]
Controller
No computational overhead
but no guarantees
Use time-varying bounds on the agent’s actions to avoid suboptimal state-action pairs
Chart: 
| 2.5 | 1.5 | 1.5 | 1.5 | 0.5 | 0.5
Y-values | 29 | 200 | 175 | 107 | 204 | 174
”Days of data” to converge to industrial rule-based performance
Classical DRL
Notes: Explain the dots

## Slide 20: Computationally Efficient RL [7]
Controller
No computational overhead
but no guarantees
Use time-varying bounds on the agent’s actions to avoid suboptimal state-action pairs
Chart: 
| 2.5 | 1.5 | 1.5 | 1.5 | 0.5 | 0.5
Y-values | 29 | 200 | 175 | 107 | 204 | 174
”Days of data” to converge to industrial rule-based performance
Classical DRL
Reward shaping (RS)

## Slide 21: Computationally Efficient RL [7]
Controller
No computational overhead
but no guarantees
Use time-varying bounds on the agent’s actions to avoid suboptimal state-action pairs
Chart: 
| 2.5 | 1.5 | 1.5 | 1.5 | 0.5 | 0.5
Y-values | 29 | 200 | 175 | 107 | 204 | 174
”Days of data” to converge to industrial rule-based performance
Classical DRL
Reward shaping (RS)
Tighter constraints
More knowledge

## Slide 22: Computationally Efficient RL [7]
Controller
No computational overhead
but no guarantees
Use time-varying bounds on the agent’s actions to avoid suboptimal state-action pairs
Chart: 
| 2.5 | 1.5 | 1.5 | 1.5 | 0.5 | 0.5
Y-values | 29 | 200 | 175 | 107 | 204 | 174
”Days of data” to converge to industrial rule-based performance
Classical DRL
Reward shaping (RS)
Tighter constraints
More knowledge

## Slide 23: Computationally Efficient RL [7]
Chart: 
| 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 1.5 | 1.5 | 1.5 | 0.5 | 0.5
Y-values | 109 | 116 | 53 | 90 | 31 | 41 | 29 | 29 | 200 | 175 | 107 | 204 | 174
Controller
No computational overhead
but no guarantees
Up to 6-7x better sample complexity than classical DRL
Use time-varying bounds on the agent’s actions to avoid suboptimal state-action pairs
”Days of data” to converge to industrial rule-based performance
Classical DRL
Reward shaping (RS)
EAs (ours)
Up to 2-3x better sample complexity than RS
Tighter constraints
More knowledge

## Slide 24: Key takeaways
Neural Networks are powerful but physics-agnostic
PiNNs for modeling
You can try different informative loss functions
If possible, you can try tailored architectures like PCNNs
PiNNs for control
You can try different reward functions and residual learning techniques
Shielding can give guarantees but is usually complex
Notes: For control Many ways to help agents online (reward shaping, residual learning, shielding, …)

## Slide 25: Thank you for your attention!
Loris DI NATALE
Urban Energy Systems Lab, Empa
Laboratoire d’Automatique, EPFL
References
[1] Di Natale, L., Svetozarevic, B., Heer, P., & Jones, C. N. (2022, June). Near-optimal deep reinforcement learning policies from data for zone temperature control. In 2022 IEEE 17th International Conference on Control & Automation (ICCA) (pp. 698-703). IEEE.
[2] Geirhos, R., Jacobsen, J. H., Michaelis, C., Zemel, R., Brendel, W., Bethge, M., & Wichmann, F. A. (2020). Shortcut learning in deep neural networks. Nature Machine Intelligence, 2(11), 665-673.
[3] Di Natale, L., Svetozarevic, B., Heer, P., & Jones, C. N. (2023). Towards scalable physically consistent neural networks: An application to data-driven multi-zone thermal building models. Applied Energy, 340, 121071.
[4] Greydanus, S., Dzamba, M., & Yosinski, J. (2019). Hamiltonian neural networks. Advances in neural information processing systems, 32.
[5] Cranmer, M., Greydanus, S., Hoyer, S., Battaglia, P., Spergel, D., & Ho, S. (2020). Lagrangian neural networks. arXiv preprint arXiv:2003.04630.
[6] Di Natale, L., Svetozarevic, B., Heer, P., & Jones, C. N. (2022). Physically consistent neural networks for building thermal modeling: theory and analysis. Applied Energy, 325, 119806.
[7] Di Natale, L., Svetozarevic, B., Heer, P., & Jones, C. N. (2022). Efficient Reinforcement Learning (ERL): Targeted Exploration Through Action Saturation. arXiv preprint arXiv:2211.16691.
loris.dinatale@empa.ch
https://www.empa.ch/web/dilo

## Slide 26: Appendix

## Slide 27: Key takeaways
Neural Networks are powerful but physics-agnostic
PiNNs for modeling
You can try different informative loss functions
If possible, you can try tailored architectures like PCNNs
PiNNs for control
You can try different reward functions and residual learning techniques
Shielding can give guarantees but is usually complex
Notes: For control Many ways to help agents online (reward shaping, residual learning, shielding, …)

## Slide 28: Key takeaways
Neural Networks are powerful but physics-agnostic – but solutions exist!
PiNNs for modeling – supervised learning
  Implementing a physical loss can be easy and might help but tuning the weighting factor is not trivial
  Use tailored architectures when possible
    PCNNs for example attain state-of-the-art accuracy for building thermal modeling while ensuring physical consistency
PiNNs for control – reinforcement learning
  While reward shaping and residual learning are easy, they might not enforce knowledge
  Shielding can preserve prior specifications but is often computationally expensive
    Enforcing simple rules instead can already help without computational overhead
Conclusion
Use (a combination of) these techniques to improve your NNs
Notes: For control Many ways to help agents online (reward shaping, residual learning, shielding, …)

## Slide 29: PiNNs for reinforcement learning
Learning through interaction with the environment
Reward shaping: modify the feedback to the network
Residual learning: additive, multiplicative, time varying, …
Shielding: Define a filter to correct the agent when some specifications are not met
  Project on the desired set
  Use a known fallback controller
Can always pretrain NNs, learn from demonstrations, …
Controller
Environment
Offline training
copy
Notes: Might be interesting if you know the output is some combination of three variables e.g. – encourages the NN to find these variables and then predict the output from them

## Slide 30: PiNNs for supervised learning
Given a dataset
Main idea: Modified loss function to steer the NN towards expected solutions
  Boundary conditions
  Physical laws (energy/mass conservation, …)
Can augment the NN’s output
backpropagation
Model
Physics-inspired NNs (PiNNs)
Notes: Learning from scratch is the usual way
Here say physics but can be any type of knowledge really

## Slide 31: PiNNs for supervised learning
Given a dataset
Main idea: Modified loss function to steer the NN towards expected solutions
  Boundary conditions
  Physical laws (energy/mass conservation, …)
Can augment the NN’s output
backpropagation
Model
Physics-inspired NNs (PiNNs)
Notes: Learning from scratch is the usual way

## Slide 32: PiNNs for supervised learning
Given a dataset
Main idea: Modified loss function to steer the NN towards expected solutions
  Boundary conditions
  Physical laws (energy/mass conservation, …)
Can augment the NN’s output
backpropagation
Model
Physics-inspired NNs (PiNNs)
Notes: Learning from scratch is the usual way

## Slide 33: PiNNs for supervised learning
Given a dataset
Main idea: Modified loss function to steer the NN towards expected solutions
  Boundary conditions
  Physical laws (energy/mass conservation, …)
Can augment the NN’s output
Can create a bottleneck
backpropagation
Model
Physics-inspired NNs (PiNNs)
Notes: Z_i typically unmeasured / unobserved variable

## Slide 34: PiNNs for supervised learning
Given a dataset
Main idea: Modified loss function to steer the NN towards expected solutions
  Boundary conditions
  Physical laws (energy/mass conservation, …)
Can augment the NN’s output
Can create a bottleneck
…
backpropagation
Model
Physics-inspired NNs (PiNNs)
Notes: Might be interesting if you know the output is some combination of three variables e.g. – encourages the NN to find these variables and then predict the output from them
Typically nice when you know there are some relationships between the outputs
Just examples – can do essentially anything, just put what you knoe in the network, and potentially modify the loss function

## Slide 35: The issue of shortcut learning
Case study on UMAR: learn the thermodynamics of buildings
PiNNs and LSTMs have a great accuracy on the validation data
Issue of shortcut learning
No impact of heating/cooling!
Notes: If want something that works in heating and cooling either wait 6 months or use a model

## Slide 36: Physically Consistent NNs (PCNNs)
Enforce physical properties by design in a module running in parallel of the NN
Building thermodynamics example
We want to ensure:
The predicted temperatures increase when the applied heating power or the outside temperature increases;
Physically meaningful energy flows between the thermal zones.
This is hard-encoded in the physics-inspired module, which processes the power inputs, ambient temperatures, and energy exchanges between the zones.
The parameters are learned from data
*
*

## Slide 37: Solving the shortcut learning issue
Case study on UMAR: learn the thermodynamics of buildings
PiNNs and LSTMs have a great accuracy on the validation data – PCNNs are physically consistent by construction
Notes: If want something that works in heating and cooling either wait 6 months or use a model

## Slide 38: Solving the shortcut learning issue
Case study on UMAR: learn the thermodynamics of buildings
PiNNs and LSTMs have a great accuracy on the validation data – PCNNs are physically consistent by construction
But they also outperform all the other physically consistent methods by 17-35%
Notes: If want something that works in heating and cooling either wait 6 months or use a model

## Slide 39: Simulation
DRL agents converge to behaviors similar to the optimal trajectories (computed a posteriori)
  Confirmed by statistical analysis over 2000 3-day long sequences
  And for different reward functions and random seeds

## Slide 40: Experiment
Only short period because of connection issues
But the agent shows similar behavior as in simulation
  Preheating
  Close to lower bound
Connection
lost

## Slide 41: An issue of convergence speed
3 years worth of data (randomly sampled days) to obtain the performance of classical rule-based controllers
15 years (500k points) to “converge”
(D)RL is usually (very, very, very) data-inefficient
High computational burden
Limited deployment on physical systems
Introduction
100k steps
Roughly 3 years worh of data
Notes: If want something that works in heating and cooling either wait 6 months or use a model

## Slide 42: Why?
Postulate
Prior expert knowledge often provides intuition about what optimal policies should do
We can accordingly constrain the agents to regions of the state space that are deemed interesting
Introduction
To get there…
… we need this!
Exploration is necessary
… but often stupid!
Notes: If want something that works in heating and cooling either wait 6 months or use a model

## Slide 43: Proposed approach to accelerate learning
Methods
Agent
x
A
x
How can we constrain the actions of agents to explore interesting states?
Design handcrafted simple rules from expert knowledge to ensure meaningful actions
Saturate the agents’ actions according to these rules
Modify the gradient update of the policy to let it learn from the corrections and steer it towards expected behaviors
Proposed approach
Notes: If want something that works in heating and cooling either wait 6 months or use a model

## Slide 44: Proposed approach to accelerate learning
Methods
How can we constrain the actions of agents to explore interesting states?
Correct the agents using safe action sets
Design handcrafted simple rules from expert knowledge to ensure meaningful actions
Saturate the agents’ actions according to these rules
Modify the gradient update of the policy to let it learn from the corrections and steer it towards expected behaviors
Each step is easy to implement and computationally inexpensive
- but no need to always satisfy these artifical constraints!
Notes: If want something that works in heating and cooling either wait 6 months or use a model

## Slide 45: What does the saturation do?
Introduction
To get there…
… we need this!
Meaningful exploration
Notes: If want something that works in heating and cooling either wait 6 months or use a model

## Slide 46: Does it impact performance?
Results
The learnt behaviors are similar!
Good final performance

## Slide 47: Does it accelerate learning?
Results
Smaller n
tighter constraints
Impact of m on EAs (ours) – more freedom
Reward Shaping (RS)
Efficient Agents (EAs) (ours)
Classical Agents
Main metric: number of days of data required to converged to the performance of industrial baselines

## Slide 48: Does it accelerate learning?
Results

## Slide 49: Does it accelerate learning?
Results
Objective attained! Up to 6-7x faster

## Slide 50: Discussion & Conclusion
Black-box models can be misleading, even if they fit the data well
  PCNNs as a potential solution - easy to scale
Deep Reinforcement Learning provides good results when coupled with PCNNs
It is possible to design simple rules based on prior knowledge to help (D)RL agents converge faster
  Saturate the actions of the agents accordingly
  Modify the gradient update to let agents learn from it
 Fully black-box pipeline from data to control policies
Wrap-up
 Avoid tedious engineering
 Energy savings of 25-30%
 Comfort of the occupants improved
 “Plug & Play” controllers
Straightforward implementation
Computationally inexpensive
 Up to 6-7 times faster

## Slide 51: Discussion & Conclusion
Neural Networks can be misleading, even if they fit the data well
  PCNNs as a potential solution - easy to scale
Deep Reinforcement Learning provides good results when coupled with PCNNs
It is possible to design simple rules based on prior knowledge to help (D)RL agents converge faster
  Saturate the actions of the agents accordingly
  Modify the gradient update to let agents learn from it
 Fully black-box pipeline from data to control policies
Wrap-up
State-of-the-art accuracy
Physical consistency
 Energy savings of 25-30%
 Comfort of the occupants improved
 “Plug & Play” controllers
Straightforward implementation
Computationally inexpensive
 Up to 6-7 times faster

## Slide 52: Main references
PCNNs
Towards Scalable Physically Consistent Neural Networks: an Application to Data-driven Multi-zone Thermal Building Models. L. Di Natale, B. Svetozarevic, P. Heer, and C.N. Jones (2022). Manuscript submitted to Applied Energy. https://arxiv.org/abs/2212.12380.
Physically consistent neural network building models: theory and analysis. L. Di Natale, B. Svetozarevic, P. Heer, and C.N. Jones (2022). Applied Energy, 119806. https://doi.org/10.1016/j.apenergy.2022.119806.
DRL
Efficient Reinforcement Learning (ERL): Targeted Exploration Through Action Saturation. L. Di Natale, B. Svetozarevic, P. Heer, and C.N. Jones (2022). Manuscript submitted to L4DC 2023. https://arxiv.org/abs/2211.16691.
Near-optimal Deep Reinforcement Learning Policies from Data for Zone Temperature Control. L. Di Natale, B. Svetozarevic, P. Heer, and C.N. Jones (2022). 2022 IEEE 17th International Conference on Control & Automation (ICCA), 698-703. https://doi.org/10.1109/ICCA54724.2022.9831914.